## Slide 1: Performance Enhancement For Spiral Indcutors, Design And Modeling
Efe Öztürk

## Slide 2
Introduction
Loss Mechanism in Inductors
Ways to improve quality
Conclusion
Contents

## Slide 3
Important inductor parameters
  Inductance value
  Self resonance frequency
  Quality factor
With a low-Q inductor :
  Increased phase noise in oscillators
  High insertion loss in filters & baluns
  High power consumption in amplifiers
  Poor I/O impedance matching
Introduction

## Slide 4
Desired Inductance value : Ls
Metal sheet resistance : Rs
Series feed-forward capacitance or sum of all overlap capacitance: Cs
Loss Mechanism

## Slide 5
Spiral to substrate capacitance : Cox
Substrate capacitance : Csi
Substrate resistance : Rsi
Loss Mechanism

## Slide 6
Eddy current components, skin effects, proximity effects : R1 & L1
  On substrate
  On metal trace
Loss Mechanism

## Slide 7
1) Eddy Currents
  On substrate
  On metal trace
2) Skin Effect
3) Proximity Effect
 Rs & Substrate loss increases
Eddy Currents [ref.17]

## Slide 8: Spiral Inductor Lumped Modeling
Maximum Attainable Q
< 1
< 1

## Slide 9: Spiral Inductor Lumped Modeling
Maximum Attainable Q
< 1
< 1
Increase Rp
Reduce Rs
Reduce Cox
Reduce Cs

## Slide 10
Physical Properties (width, spacing...)
Patterned Ground Shield (PGS)
Metal Stack, Thicker Metal Layer
High Resistivity Substrates
New inductor models
Oxide Etching
Ways to improve Q

## Slide 11
Play with substrate !
  High resistivity substrate (Glass with relative permitivity: 5-6):
    high Rsub (compared to Si)
    Reduced Csub (compared to Si)
    Impedance of the substrate network simply reduces to a single capacitance dominated by the smaller between Cox and Csub
Ways to improve Q
1-High Resistivity Substrate [ref.2]

## Slide 12
Play with substrate !
  Increase Rp (Rsub)
  Reduce Cp (Csub+Cox)
Polymer underneath (perm:2.75)
  Higher resistivity ( high Rp)
  Lower permitivity ( low Cp)
Ways to improve Q
2-Polymer Cavity [ref.15]

## Slide 13
Series feed-forward capacitance or sum of all overlap capacitance, metal to metal cap, Cs
Ways to improve Q
3-Change Model [ref.10]

## Slide 14
Remove the oxide layer between the spiral and substrate by an optimized etching tech.
  Improve the insulation to inductor
  Relative permitivity becomes 1 (vacuum)
  Cox capacitance minimized
  Reduced substrate effect
Ways to improve Q
4-Oxide Etching [ref.4]

## Slide 15
Increase metal thickness for high-Q :
  Increased metal sidewall areas of current
  Decreased metal resistance, Rs
Stack the metals :
  Combine metal layers through vias
  Decreased metal resistance, Rs
Ways to improve Q
5-Metal Thickness & Stack [ref.18]

## Slide 16
Substrate Loss Factor approaches to unity as Rpinf.
Rp approaches to inf. as Rsiinf. or Rsi0.
Patterned Groung Shielding acts as a short.
Slotted pattern reduces the negative mutual coupling. The slots act as open circuit. Prevents the build up of image current
 Q,NGS < Q,SGS < Q,PGS
* NGS: no ground shield
* SGS: solid groung shield
* PGS: patterned ground shield
Ways to improve Q
6-Patterned Groung Shielding [ref.9]

## Slide 17
To improve factor :
  Reduce Rs
  Increase Rsub
  Reduce Csub
  Reduce Cox
  Reduce Cs
Summary